Art. No. 341047 - 341026		                                       ECLIPS TWIN QR111

Description:

The ECLIPS is a recessed fixture for double lamps which fits into the range of the ECLIPS fittings. The fixture is easy to install with 4 torsion springs. The frame has an oval shape. The complete body & lamprings are 100% made out of aluminium.

The Fixture exists in 2 finishes; textured white powdercoated & textured black powdercoated..

Installation frames and boxes are also available.

TAL – Essentials collection

Electrical data:

Lamp type: 	QR111 20-100W

Lamps: 	2

Lampholders: 	G53

Control gear: 	Remote transfo

Input supply voltage: 	12V-50Hz

Connector block: 	2x2,5mm²

Glow wire resistance:	960°
IP rating: 	IP20	 	
Protection classification:

Mounting surface classification:

Approvals:

Materials and finish

Housing and lamprings: 100% Aluminium (AlMgSi0,5) + powdercoated

Installation and lamp replacement:

The luminaire fits into an oval hole into the ceiling and is hold by 4 torsion springs.

Lamp replacement is very easy by just pulling on the lamps (hold by springs), and unscrewing the G53 socket

Technical data

Cut-out:	  2X diameter 158 with center distance of 140mm

Installation height :	115mm

Luminaire dimensions:  	318X178X115mm

Weight: 	2,5 kg

Adjustability: 	Lamp can be oriented in all directions by gimble system

Accessories:	341077 – Installation Box for plaster

341097 – Installation Box for concrete